4/14/2006

1999 TERRY TRAILER WINTERIZING INSTRUCTIONS

STEP 1:	DRAIN HOLDING TANKS

Drain fresh, gray, & black water tanks (open faucet to vent)

STEP 2:	HOT WATER TANK

Drain hot water tank, turn off heater element by tank (open faucet)

STEP 3:	CONNECT ANTI-FREEZE

Switch winterize bypass valve to bypass (up?)

Remove brass cap and screw bypass hose on to gold valve and other end into gallon jug of antifreeze

STEP 4:	BYPASS HOT WATER TANK

Turn on trailer pump

Pump a little bit of antifreeze into hot water tank (it’s ok for it to drain out)

Bypass hot water tank (big blue handle)

STEP 5:	FLUSH LINES W ANTIFREEZE

Open taps one by one until antifreeze appears – do hot and cold taps – sinks, toilet, tub, outside shower - start with kitchen sink (longest run)

STEP 6:	CITY WATER CONNECTION

Turn OFF water pump and open a cold water tap

Pry out screen and washer at city water connection

Push in on valve stem until antifreeze runs out

STEP 7:	DRAINS

Dump holding tanks

Pour a cupful of antifreeze into every drain

Pour a pint of antifreeze directly through toilet and tub drain

All Done!